## Slide 1: Grain Size Distribution
Allen Bateman Pinzón ---- Curso …… 2014/2015

## Slide 2: Grain Size Distribution slides from Gary PArker
CHARACTERIZATION OF SEDIMENT AND GRAIN SIZE DISTRIBUTIONS
For sufficiently coarse particles, the “diameter” D is often defined to be the dimension of the smallest square mesh opening through which the particle will pass. For finer particles, “diameter” D often denotes the diameter of the equivalent sphere with the same fall velocity vs [L/T] as the actual particle.
Grain size is often specified in terms of a
base-2 logarithmic scale (phi scale or psi scale).
These are defined as follows: where D is given in mm
Allen Bateman Pinzón ---- Curso …… 2014/2015

## Slide 3: Título/Capítulo
SAMPLE EVALUATIONS OF  AND 
D (mm) |  | 
4 | 2 | -2
2 | 1 | -1
1 | 0 | 0
0.5 | -1 | 1
0.25 | -2 | 2
0.125 | -3 | 3
Allen Bateman Pinzón ---- Curso …… 2014/2015
Grain Size Distribution

## Slide 4: Grain Size Distribution
Mineral clays such as smectite, montmorillonite and bentonite are cohesive, i.e. characterized by electrochemical forces that cause particles to stick together. Even silt-sized particles that are do not consist of mineral clay often display some cohesivity due to the formation of a biofilm.
SEDIMENT SIZE RANGES
Allen Bateman Pinzón ---- Curso …… 2014/2015

## Slide 5: Título/Capítulo
SEDIMENT GRAIN SIZE DISTRIBUTIONS
The grain size distribution is characterized in terms of N+1 sizes Db,i such that ff,i denotes the mass fraction in the sample that is finer than size Db,i.
i | Db,i mm | ff,i
1 | 0.03125 | 0.020
2 | 0.0625 | 0.032
3 | 0.125 | 0.100
4 | 0.25 | 0.420
5 | 0.5 | 0.834
6 | 1 | 0.970
7 | 2 | 0.990
8 | 4 | 1.000
Note the use of a logarithmic scale for grain size.
Allen Bateman Pinzón ---- Curso …… 2014/2015
Grain Size Distribution

## Slide 6: Título/Capítulo
SEDIMENT GRAIN SIZE DISTRIBUTIONS contd.
In the last slide, the finest size (0.03125 mm) was such that 2 percent was finer. If the finest size does not correspond to 0 percent content, or the coarsest size to 100 percent content, it is often useful to use linear extrapolation on the psi scale to determine the missing values.
Allen Bateman Pinzón ---- Curso …… 2014/2015
Grain Size Distribution
Log (D)
Extrapolation

## Slide 7: Título/Capítulo
SEDIMENT GRAIN SIZE DISTRIBUTIONS contd.
i | Db,i mm | ff,i
1 | 0.03125 | 0.020
2 | 0.0625 | 0.032
3 | 0.125 | 0.100
4 | 0.25 | 0.420
5 | 0.5 | 0.834
6 | 1 | 0.970
7 | 2 | 0.990
8 | 4 | 1.000
i | Db,i mm | ff,i
1 | 0.0098 | 0
2 | 0.03125 | 0.020
3 | 0.0625 | 0.032
4 | 0.125 | 0.100
5 | 0.25 | 0.420
6 | 0.5 | 0.834
7 | 1 | 0.970
8 | 2 | 0.990
9 | 4 | 1.000
Note that the addition of the extra point has increased N from 8 to 9 (there are N+1 points).
Allen Bateman Pinzón ---- Curso …… 2014/2015
Grain Size Distribution

## Slide 8: Título/Capítulo
SEDIMENT GRAIN SIZE DISTRIBUTIONS contd.
The grain size distribution after extrapolation is shown below.
i | Db,i mm | ff,i
1 | 0.0098 | 0
2 | 0.03125 | 0.020
3 | 0.0625 | 0.032
4 | 0.125 | 0.100
5 | 0.25 | 0.420
6 | 0.5 | 0.834
7 | 1 | 0.970
8 | 2 | 0.990
9 | 4 | 1.000
Allen Bateman Pinzón ---- Curso …… 2014/2015
Grain Size Distribution

## Slide 9: Título/Capítulo
CHARACTERISTIC SIZES BASED ON PERCENT FINER
Dx is size such that x percent of the sample is finer than Dx
Examples:
D50 = median size
D90 ~ roughness height
Allen Bateman Pinzón ---- Curso …… 2014/2015
Grain Size Distribution

## Slide 10: Título/Capítulo
CHARACTERISTIC SIZES BASED ON PERCENT FINER
To find Dx (e.g. D50) find i such that
Then interpolate for x
and back-calculate Dx in mm
Allen Bateman Pinzón ---- Curso …… 2014/2015
Grain Size Distribution

## Slide 11: Título/Capítulo
STATISTICAL CHARACTERISTICS OF SIZE DISTRIBUTION
i (Di) = characteristic size of ith grain size range
fi = fraction of sample in ith grain size range
Allen Bateman Pinzón ---- Curso …… 2014/2015
Grain Size Distribution

## Slide 12: Título/Capítulo
STATISTICAL CHARACTERISTICS OF SIZE DISTRIBUTION contd.
Dg = 0.273 mm, g = 2.17
= mean grain size on psi scale
 = standard deviation on psi scale
Dg = geometric mean size
g = geometric standard deviation (  1)
Sediment is well sorted if g < 1.6
Allen Bateman Pinzón ---- Curso …… 2014/2015
Grain Size Distribution

## Slide 13: Título/Capítulo
Example: WHY CHARACTERIZE GRAIN SIZE DISTRIBUTIONS IN TERMS OF
A LOGARITHMIC GRAIN SIZE?
Consider a sediment sample that is half sand, half gravel (here loosely interpreted as material coarser than 2 mm), ranging uniformly from 0.0625 mm to 64 mm. Plotted with a logarithmic grain size scale, the sample is correctly seen to be half sand, half gravel. Plotted using a linear grain size scale, all the information about the sand half of the sample is squeezed into a tiny zone on the left-hand side of the diagram.
Logarithmic scale for grain size
Linear scale for grain size
Allen Bateman Pinzón ---- Curso …… 2014/2015
Grain Size Distribution

## Slide 14: Título/Capítulo
Allen Bateman Pinzón ---- Curso …… 2014/2015
UNIMODAL AND BIMODAL GRAIN SIZE DISTRIBUTIONS
The fractions fi(i) represent a discretized version of the continuous function f(), f denoting the mass fraction of a sample that is finer than size . The probability density pf of size  is thus given as p = df/d.
The example to the right corresponds to a Gaussian (normal) distribution with:
= -1 (Dg = 0.5 mm) and
 = 0.8 (g = 1.74)
Grain Size Distribution

## Slide 15: Título/Capítulo
Allen Bateman Pinzón ---- Curso …… 2014/2015
UNIMODAL AND BIMODAL GRAIN SIZE DISTRIBUTIONS
The probability density pf of size  is given as p = df/d.
The grain size distribution is called unimodel because the function p() has a single mode, or peak.
The following approximations
are valid for a Gaussian distribution:
Grain Size Distribution

## Slide 16: Título/Capítulo
Allen Bateman Pinzón ---- Curso …… 2014/2015
UNIMODAL AND BIMODAL GRAIN SIZE DISTRIBUTIONS contd.
A sand-bed river has a characteristic size of bed surface sediment (D50 or Dg) that is in the sand range.
The grain size distributions of most sand-bed streams are unimodal, and can often be approximated with a Gaussian function.
Many gravel-bed river, however, show bimodal grain size distributions, as shown to the upper right. Such streams show a sand mode and a gravel mode, often with a paucity of sediment in the pea-gravel size (2 ~ 8 mm).
A bimodal (multimodal) distribution can be recognized in a plot of f versus  in terms of a plateau (multiple plateaus) where f does not increase strongly with .
Grain Size Distribution

## Slide 17: Título/Capítulo
Allen Bateman Pinzón ---- Curso …… 2014/2015